## Slide 1: Human Impact on Health and Environmental Water Sustainability
<number>
P.G. Lokkas
G. Papapolymerou
(TEI) of Larissa, GREECE
Rhodes, Greece, July 4-7, 2004
EURO XX CONFERENCE
by
Notes: <number>

## Slide 2: Environmental Engineering Problems
Rhodes, Greece, July 4-7, 2004
<number>
Environmental engineering addresses problems in the:
water
air and
soil environments

## Slide 3: The European Commission Policy
Rhodes, Greece, July 4-7, 2004
<number>
Provision of a secure supply of a safe drinking water in sufficient quantity,
Provision of water resources of sufficient quality and quantity, to meet other economic requirements of industry and agriculture,
Quality and quantity of water resources sufficient to protect and sustain the good ecological state and functioning of the aquatic environment,
Management of water resources to prevent or reduce the impact of floods and minimise the effects of droughts.

## Slide 4: The Role of Engineers and Scientists
Rhodes, Greece, July 4-7, 2004
<number>
Public works have traditionally been seen as civil engineering activities. Such works may be:
  water supply.
  sewage disposal schemes.
Most water engineering works involve large structures and require a good understanding of hydraulics.
Water science and technology typically involve the application of biological, chemical and physical principles along with engineering techniques.

## Slide 5: Water Quality Control
Rhodes, Greece, July 4-7, 2004
<number>
A major objective in developing Countries is to reduce the incidence of water-related diseases.
In Industrialized Countries the problem is to provide water free of heavy metals and other chemicals that endanger human health and to insure an adequate supply of it.

## Slide 6: Healthy Water
Rhodes, Greece, July 4-7, 2004
<number>
The water is biologically healthy when it is free from pathogenic microorganisms.
Other important considerations are:
Visible suspended matter
colour, taste and odour
Objectionable dissolved matter

## Slide 7: Supplementary Necessities
Rhodes, Greece, July 4-7, 2004
<number>
Convey the supply to consumers through a distribution system, consisting of water mains, pumping stations etc.
In cases where treated wastewaters provide a large proportion of the water resources for other users,before releasing water of domestic and industrial uses to the environment.
  Collection of wastewater which is produced.
  Suitable treatment of water.

## Slide 8: Requirements and Constraints of Quality Management
Rhodes, Greece, July 4-7, 2004
<number>
Water quality control measures must balance between the needs of water supply services and the requirements of effluent discharge.
Various factors must be recognized in a situation where industrial activity, changing agricultural practices can increase urbanization and influence the water quality.

## Slide 9: Major Environmental Problems
Rhodes, Greece, July 4-7, 2004
<number>
Big cities produce large volumes of solid wastes, in their disposal.
Landfills and other solid waste disposal sites may be responsible for water pollution since rainfall or groundwater can leach highly contaminating substances from the deposited materials.
There is a need of what can be termed ‘clean technology’. Therefore:
  Attention for a reduction of packaging material.
  Recovery and re-use of other waste materials.

## Slide 10: The Role of the Environmental Professional
Rhodes, Greece, July 4-7, 2004
<number>
Make design and management decisions so that they allow the use of environment without a negative effect.
Apply restrictions for discharges from human activity into the air, the water or soil, because each of these potential reservoirs can accept only a limited amount of physical, chemical or biological substances without deterioration.
facilitation of sustainable growth.

## Slide 11: The Environmental Deterioration
Rhodes, Greece, July 4-7, 2004
<number>
It may be caused through a variety different ways:
weather.
  wind (dust blown in the air).
  rain (storm water eroding soil into the water and floods depositing solids).
  lighting (fires discharging smoke and particulates into the air and water along with ash on to the soil).

## Slide 12: The Environmental Deterioration
Rhodes, Greece, July 4-7, 2004
<number>
volcanoes (smoke and particulates into the air water and soil),
vegetation (hydrocarbon vapours discharged into the air and dissolved hydrocarbons running into the water),
animals (faeces polluting the water),
activities of humans.

## Slide 13: The Soil Pollution
Rhodes, Greece, July 4-7, 2004
<number>
The discharge of pollutants onto or into the soil is of local concern (liquid migrations in soil is slow).
It is of concern when the pollutant is liquid or is a soluble solid (an insoluble solid will not migrate nor will it dissolve into the groundwater).
The major concern is the subsequent pollution of the groundwater when it is used as a source for drinking, irrigation or industrial use.

## Slide 14: Classification of Pollutants
Rhodes, Greece, July 4-7, 2004
<number>
The pollutants, in order to predict their effects on water quality and the means of their removal, can be classified as:
Solid.
Liquid.
Gas.
One of these, mixed with or dissolved in another.

## Slide 15: Classification of Pollutants
Rhodes, Greece, July 4-7, 2004
<number>
Each of these can be organic or inorganic.
An organic waste can additionally be classified as volatile or non-volatile, biodegradable and non-biodegradable, toxic or of limited toxicity.
Inorganic wastes should be further classified as dissolved, suspended or coarse (ability to settle quickly), of mineral and non-mineral origin, toxic or of limited toxicity.

## Slide 16
Rhodes, Greece, July 4-7, 2004
<number>
BASIC
STATE
MIXED
STATE
SUB
STATE
EXAMPLE
Solid
Solid
Organic
Sugar
Inorganic
Salt
Solid in liquid
Organic
Food processing waste
Inorganic
Electroplating Waste Treatment
Solid in Gas
Organic
Plant Aerosols
Inorganic
Incinerator Particulates
Liquid
Liquid
Organic
Gasoline
Inorganic
HCl
Liquid in Solid
Organic
Garbage
Inorganic
Uncured Concrete
Liquid in Gas
Organic
Air Stripper Mist
Inorganic
Mist
Gas
Gas
Organic
Toluene
Inorganic
Air
Gas in Solid
Organic
Floats
Inorganic
Methane Storage Tank
Gas in Liquid
Organic
Anaerobic Decomposition
Inorganic
Dissolved Sir Flotation

## Slide 17: Selection of Treatment System
Rhodes, Greece, July 4-7, 2004
<number>
Parameters that must be established:
Geographical.
  the area available for the appropriate treatment needs to be addressed.
Financial.
  the budget for the project in terms of both cost and time.
Political.
  they comprise zoning, permit availability, community support and future regulatory legislation.

## Slide 18: Verification of European Parliament
Rhodes, Greece, July 4-7, 2004
<number>
The state – members, have up to a large degree, unfortunately, failed to fulfil the target of the directive concerning the nitrate pollution, namely the decrease of nitrate pollution of waters, warding off the eutrophication problem and the subsequent low quality of potable water, along with the consequences on the health of humans and animals.

## Slide 19: The Situation in Greece
Rhodes, Greece, July 4-7, 2004
<number>
It is marked, specifically for Greece, that there is a large delay in instituting the necessary measures of implementation of the corresponding directive, in spite the fact that the state - member had admitted the existence of eutrophication problems in some bays.

## Slide 20
Rhodes, Greece, July 4-7, 2004
<number>
GREECE

## Slide 21: The Situation in THESSALY
Rhodes, Greece, July 4-7, 2004
<number>
The greater area of Thessaly today faces the the following problems:
Nitrates in drinking water, which, essentially all emanate from agricultural activities.
Pesticides from run off
The lowering of the water table
Other chemicals, mainly from olive-oil producing factories and textile dying
Seepage of wastewater from unlicensed rubbish-dumps
Floods from deforestation and closing of natural water-way flows

## Slide 22
Rhodes, Greece, July 4-7, 2004
<number>
NITRATES:
The problem is more severe in South-Central Thessaly
Nitrate concentration has been measured in excess of 80 mg/l in several localities and values of 200-300 mg/l have been measured in some samples. Upper limit: 50 mg/l
Problem is severe in an area 20-30 Km wide by 40-50 Km long stretching South from Larisa to Farsala
There is a so called denitrification program that is been tried with encouraging early results

## Slide 23: DENITRIFICATION PROGRAM
<number>
Replacement of fertilizer intensive crops by tree farms
Total Replacement of fertilizer intensive crops by animal grazing fields
Reduction in the use of nitrogen based fertilizers
Replacement of current crops

## Slide 24: PESTICIDE RUN OFF
<number>
The Problem arises from the excessive agricultural use of the land especially from cotton growing
Run off ends in rivers and then in the sea
Pesticides have been measured in fish tissue in the sea but values are below 5 ppb.
The use of fine spray equipment causes transport of pesticides in nearby villages.
Studies are underway to determine potential risk to health

## Slide 25: LOWERING OF THE WATER TABLE
<number>
Alternative Crops
Alternative technologies for irrigation
Creation of many small dams and small lakes
Reverse pumping

## Slide 26: Other Chemicals
Rhodes, Greece, July 4-7, 2004
<number>
Heavy Metals
Phenolic Compounds
Dyes
PCB’s
Solvents

## Slide 27: HEAVY METALS
<number>
Electroplating Industries. Problem: small units that do not have capability in managing these toxic waste.
Anodizing. Problem: Usually treatment is not satisfactory and waste is simply stored at the site
Steel manufacturing and metal processing. Problem: heavy metals are found in wastewater, usually end up in the sea

## Slide 28: WASTEWATER FROM OLIVE PROCESSING
<number>
Currently there is not an efficient technology for treating it.
Wastewaters are toxic with a high COD/BO ratio
It is directed on small creeks and rivers
Problem throughout Greece
One technology, use of Fenton’s or Fenton-like reactions, is emerging
Technology most likely to be used to pre-treat the effluents to make it compatible for biological treatment (reduce the COD/BOD ratio)

## Slide 29: DYES
<number>
High COD/BOD: 3-6
Large industrial complexes which discharge up to 600 m3/day
There is no current technology for efficient treatment
Problem is throughout Greece
Currently physical treatment clears the effluents from color
Problem with regard to disposing the mud
Photocatalysis and combined Photo-Fenton Reactions are emerftging as powerful technologies

## Slide 30: PCB’s AND SOLVENTS
<number>
Problem not as widespread
However waste is highly toxic and dangerous for the environment and the public
Solvents from various small installations
PCB’s mainly from he electric utility company
PCB’s are currently stored and subsequently are incinerated outside of Greece

## Slide 31: ANTIPOLLUTION TECHNOLOGIES
<number>
ADVANCED OXIDATION TECHNOLOGIES
Fenton and Photo-Fenton
Photocatalysis
Photo-oxidation
Chemical oxidation
Electrolytic oxidation
Thermo-chemical oxidation

## Slide 32: ANTIPOLLUTION TECHNOLOGIES
<number>
PHYSICAL PROCESSES
Absorption and Adsorption
Filtration, microfiltration and Ultrafiltration
Sedimentation
Other (over 110 emerging technologies)
THERMAL PROCESSES
1. Incineration

## Slide 33: Other Local Problems
Rhodes, Greece, July 4-7, 2004
<number>
Unrestrained dumping of rubbish on a landfill.
Although in cities of more than 10,000 inhabitants there are strictly defined places as landfills, in small villages there is always the risk of a free dumping, which may locally lead to a soil pollution with the subsequent pollution of the groundwater.

## Slide 34: Conclusions
Rhodes, Greece, July 4-7, 2004
<number>
In the 21st century, water might cause crises similar to the oil crises of the 20th century and most possibly these might be more violent.
Policies about water management must be established in order to face this serious threat to human sustained development.
Three distinct directions of education in either a local, national and International level have to be implemented:
1. Water use policy and recycling incentives
2. Water management (both ground and Surface)
3. Water treatment technologies

## Slide 35: Conclusions From the Farmers’ Point of View
Rhodes, Greece, July 4-7, 2004
<number>
1) The farmers have to be properly informed and consulted for the problems that excessive and non-rational use of fertilizers and pesticides may cause.
2) Motivations for a transfer to a biological cultivation, not only due to the lack of the use of fertilizers, but also because the biological products are healthier than the corresponding conventional.
3) A potential tax increase on the fertilizers would most possibly lead to a prudent use of nitrates, with a consequence of a reduction on the nitrate pollution.

## Slide 36: Conclusions From the Farmers’ Point of View
Rhodes, Greece, July 4-7, 2004
<number>
4) A strict application of the agricultural code of practice by the farmers would result in a proper storage of fertilizers, a rational and correct use, with specific doses for defined cultivations, on the appropriate time of fertilization.
5) A direct pollution of water masses has to be avoided. In such a case the local authorities have to be immediately informed to take precaution measures. Clear water is necessary for the living organisms.

## Slide 37: Conclusions From the Engineering Point of View
Rhodes, Greece, July 4-7, 2004
<number>
It would be essential if effective methods in training of future engineers would be developed.
A start for these methods could well be teaching in the secondary education of subjects relevant to environmental pollution and how the human health is affected.
A second step could be a campaign on the TV or in the newspapers.

## Slide 38: Conclusions From the Engineering Point of View
Rhodes, Greece, July 4-7, 2004
<number>
Finally, in the local universities or Technological Educational Institutes (TEI):
Incorporation of various technological subjects of environmental antipollution in their schedule, could be a substantial contribution.
On the top of it, the available fullest engineering and scientific information collected from different fora might be a powerful tool and assist the decision-makers to amend or complete the existing legislation.

## Slide 39: Conclusions From the Engineering Point of View
Rhodes, Greece, July 4-7, 2004
<number>
In regions with low population, creation of water quality control centres, which test chemically and microbiologically the waters of the local area, could guarantee a safe quality of potable water.
It should be worth noting a phrase written in a memorandum with aspects for waters:
Just think of what the future is going to be, taking into account that the fish, being unable to live on the ground, has already started to die into the water.

## Slide 40
Rhodes, Greece, July 4-7, 2004
<number>
Thank you